## Slide 1: VLAN

## Slide 2: Virtual LANs (VLANs)
Definition: A logical grouping of network users and resources connected to administratively defined ports on a switch.
  Smaller broadcast domains
  Organized by:
    Location
    Function
    Department
    Application or protocol

## Slide 3: Switches

## Slide 4: Features of VLANs
Simplify network management
Provides a level of security over a flat network
Flexibility and Scalability

## Slide 5: Flat Network Structure

## Slide 6: Security
Flat network problems
VLANs

## Slide 7: Flexibility & Scalability
Layer-2 switches only read frames
  Can cause a switch to forward all broadcasts
VLANs
  Essentially create broadcast domains
    Greatly reduces broadcast traffic
    Ability to add wanted users to a VLAN regardless of their physical location
    Additional VLANs can be created when network growth consumes more bandwidth

## Slide 8: VLANs Remove The Physical Boundary

## Slide 9: VLAN Memberships
Static VLANs
  Typical method of creating VLANs
  Most secure
    A switch port assigned to a VLAN always maintains that assignment until changed
Dynamic VLANs
  Node assignment to a VLAN is automatic
    MAC addresses, protocols, network addresses, etc
  VLAN Management Policy Server (VMPS)
    MAC address database for dynamic assignments
    MAC-address to VLAN mapping

## Slide 10: Identifying VLANs

## Slide 11: Identifying VLANs (cont.)

## Slide 12: VLAN Trunk Protocol (VTP)
Purpose: to manage all configured VLANs across a switch internetwork & maintain consistency
- Allows an administrator to add, delete, & rename VLANs

## Slide 13: VTP Benefits
Benefits
  Consistent configuration
  Permits trunking over mixed networks
  Accurate tracking
  Dynamic reporting
  Plug-and-Play
A VTP server must be created to manage VLANs

## Slide 14: VTP Modes

## Slide 15: VTP Modes of Operation
Server
  Default for all Catalyst switches
  Minimum one server for a VTP domain
Client
  Receives information + sends/receives updates
  Cannot make any changes
Transparent
  Does not participate in a VTP domain but forwards VTP advertisements
  Can add/delete VLANs
  Locally significant

## Slide 16: Configuring VLANs
Creating VLANs
Assigning Switch Ports to VLANs
Configuring Trunk Ports
Configuring Inter-VLAN routing